## Slide 1: QoS Automation Tool
Fernando Figliolo
Team: Breaking Bad
FLC CASA
Nov 2021

## Slide 2: Agenda
What is it?
Carrier QUEUE-DSCP Mapping
Components
Script Workflow
How it Works
Questions?

## Slide 3: What is it?
It’s a tool to setup new QoS class-map values.
  Values to be configured:
    Real Time Traffic %
    Video Class-map %
    D1 Class-map %
    D2 Class-map %
    D3 Class-map %
    D4 Class-map %
  Main parameters are Real Time and Video Class-maps to improve Skype & Zoom performance.
  It doesn’t change any other parameter like class-map names, neither policy-map (4Q, 5Q, 6Q…) or DSCP mapping.
  It doesn´t check if whole QoS configuration is correct.
The script was written in Python.

## Slide 4: Carrier QUEUE-DSCP Mapping
AT&T 4Q | AT&T 6Q | ORANGE 5Q
REAL TIME | REAL TIME | REAL TIME
D1 | VIDEO | VIDEO
D2 | D1 | D1
D3 | D2 | D2
 | D3 | D3
 | D4 | 
i.e.
AT&T 6Q Options:
10% RT, 10/10/50/25/5
20% RT, 20/10/40/25/5
20% RT, 20/10/50/15/5
20% RT, 20/10/60/5/5

## Slide 5: Components
Input module:
  Routers hostname list
  Predefined remaining QoS values option list
  User’s Input Interface:
    Real time value
    Remaining bandwidth Option Selection
Configuration module
Verification module
Output module

## Slide 6: Script Workflow
Is QoS the same type as new?
Get QoS Options
Input REAL-TIME value
Select New QoS Settings
Change QoS Settings
Get Current QoS Settings
Has QoS the same values as new?
Verify QoS Change
Not Modify
Configure New QoS Values
Not Modify
Get QoS Settings
Has QoS the same values as new?
QoS Change Success
QoS Change Failure
Input Values
Get Hosts List
Yes
Yes
Yes
No
No
No
1.
2.
3.

## Slide 7: How it Works
1_ Insert Real Time value %
2_ Choose option for remaining bandwidth distribution for each Class-Math %

## Slide 8: How it Works
3_ Enter NVS login credentials and start applying
An error found in the device configuration. Nothing is going to be applied. You should do it manually.
None of the configurations are applied as this is a demo!

## Slide 9: Questions?